## Slide 1
Objective
Develop a new algorithm for inferring reservoir operating policies from data and create a national-scale inventory of reservoir operating policies.
Approach
Collected records of daily operations for 600 large reservoirs in the United States.
Developed a new algorithm (“Storage Targets and Release Functions Inference Tool”—STARFIT) for inferring reservoir operating policies from data and extrapolating the policies to data-scarce reservoirs (“STARFITx”), building on prior research focused on the Columbia River Basin.
Simulated rules and compared performance to existing method used in large-scale hydrology.
Impact
STARFIT provides a substantial and robust improvement over existing practice.
STARFIT enables the creation of the first inventory of reservoir operations covering all large reservoirs in the United States.
STARFIT unlocks continental-scale hydrology for a range of multisectoral dynamics research applications relying on accurate water storage and release (e.g., drought and flood impacts, hydropower generation).
New Data-Driven Algorithm Improves Reservoir Simulations for National-Scale Hydrology
Turner, S.W.D., Steyaert, J.C., Condon, L., Voisin, N. “Water storage and release policies for all large reservoirs of conterminous United States” Journal of Hydrology, 603(A), 126843, (2021). [DOI: 10.1016/j.jhydrol.2021.126843]
Error (nRMSE) reduction for STARFIT (policy inferred from data) and STARFITx (policy extrapolated from nearby, similarly purposed reservoirs) relative to the popular Hanasaki generic reservoir method. Each point represents a simulated reservoir. Boxplots give the interquartile range with whiskers extending to 1.5 times the interquartile range. The STARFIT-based simulations offer substantial, robust improvements in storage simulation (~50% reduction in error on average) and release simulation (~20% reduction in error on average) relative to conventional practice.
Simulated water release
Simulated water storage
%
Error reduction relative to conventional method
STARFIT
STARFITx
STARFIT
STARFITx
Reservoir storage capacity