## Slide 1
Objective
Evaluate how rain-on-snow (RoS) events, which can lead to flooding, are represented across different historical hydrometeorological datasets and understand the factors driving discrepancies in event detection and magnitude.
Approach
Develop an objective, automated algorithm to detect RoS events by identifying concurrent precipitation, runoff, and snowmelt exceedances within a river basin.
Apply the algorithm to historical data from the Susquehanna River Basin (SRB), comparing RoS frequencies and magnitudes across four widely used hydrometeorological datasets.
Examine RoS event representation, including a detailed comparison of the benchmark January 1996 Mid-Atlantic floods, to assess differences in snowmelt and runoff.
Impact
Significant discrepancies in RoS event detection were found and datasets still only partially agreed even when accounting for daily distributions of snowmelt and runoff.
Differences in surface hydrology were identified as the primary drivers of variability, both due to land surface model characteristics and meteorological forcing frequency.
This study emphasizes the importance of selecting appropriate datasets for flood risk management and operational decision-making in regions prone to compound hydrological extremes like RoS events.
Figures: Above panels show how precipitation, snowmelt, and runoff varied during the 1996 water year across four observational products. Periods of rain-on-snow (RoS) floods are shaded in purple, with contours along the top of each panel indicating anomalous streamflow, where darker colors represent more extreme values. The figure on the right illustrates the 96-hour evolution of the 1996 SRB RoS flood in the same four datasets, highlighting differences in event representation that contribute to variability in RoS event statistics
Variability in Rain-on-Snow Event Detection: Discrepancies Across Climate Datasets
Zarzycki, C. M., Ascher, B. D., Rhoades, A. M., and McCrary, R. R.: Algorithmically detected rain-on-snow flood events in different climate datasets: a case study of the Susquehanna River basin, Nat. Hazards Earth Syst. Sci., 24, 3315–3335, https://doi.org/10.5194/nhess-24-3315-2024, 2024.