## Slide 1: Exploring multisectoral drought vulnerability in Colorado’s West Slope Basins
Patrick Reed, David Gold, Rohini Gupta
Cornell University
Theme 2: Advancing Regional Modeling to Better Capture risks and Impacts

## Slide 2: Theme 2 Risks & Impacts – Questions
Q1: What is needed to improve the decision relevance of regional projections and better capture system shocks?
Q2: What are the bottlenecks for advancing regional modeling to better capture risks and impacts?

## Slide 3: Theme 2 Risks & Impacts – What is needed
What is needed to improve the decision relevance of regional projections and better capture system shocks?
  We need to more holistically engage with the drivers and determinants of regional risks
  Better quantify highly uncertain extremes that could be experienced from both internal variability & anthropogenically forced climate changes
  Decision relevance requires representation of institutionally complex human systems (e.g., water rights & infrastructure in the US West)

## Slide 4: Theme 2 Risks & Impacts – A Broader View of risk
4
Systemic failures, extreme events and ‘hyper-risks’ emerge as a result of the highly complex and highly interconnected human-Earth systems
Dynamic relationships between agents, systems and sectors transmit risk for one to another
Drivers can amplify or buffer existing threats
Adapted from Simpson et al. (2021). https://www.cell.com/one-earth/abstract/S2590-3322(21)00179-2
Hazard
Vulnerability
Response
Exposure
RISK
+
—

## Slide 5: Theme 2 Risks & Impacts – A Broader View of risk
5
Need to Capture Compounding or Cascading Risks
Interacting risks can emerge across scales, systems, and sectors
Human responses can be strong determinants of risk
Combinations of multiple risks pose challenges for model-based insights
Figure adapted from Simpson et al. (2021). “A framework for complex climate change risk assessment”. In: One Earth 4.4,
1648 pages 489–501. ISSN: 2590-3322.

## Slide 6
Gold et al (In Revision) Earth’s Future, https://doi.org/10.22541/essoar.171466633.31829337/v1

## Slide 7: Colorado’s west Slope Basins
Lukas, J. J., & Payton, E. A. (2020). Colorado River Basin climate and hydrology: State of the science.
Nearly 70% of the inflow to Lake Powell originates in Colorado’s West Slope Basins
West Slope
Other
Arizona
New
Mexico
Utah
Colorado
Data from: US Bureau of Reclamation (2020). 1909-2020 streamflow data for the Salt and Colorado River

## Slide 8: Historical decadal droughts
Annual Flow (ft3 /year)
Annual Flow (ft3 /year)
Upper Colorado River
Gunnison River
Yampa River
White River
Southwest

## Slide 9: Historical decadal droughts
Annual Flow (ft3 /year)
Annual Flow (ft3 /year)
Upper Colorado River
Gunnison River
Yampa River
White River
Southwest
v
How could drought risks evolve for this region by 2050?

## Slide 10: A middle-of-the-road climate scenario
Hoerling et al (2024) Journal of Climate, https://doi.org/10.1175/JCLI-D-23-0617.1

## Slide 11: A middle-of-the-road climate scenario
Hoerling et al (2024) Journal of Climate, https://doi.org/10.1175/JCLI-D-23-0617.1
A mid-century average 7% reduction in outflows is relatively optimistic & middle of road

## Slide 12: Theme 2 Risks & Impacts – Better capture extremes
The modern observation record of the last century is limited in its ability to capture persistent drought extremes and the internal variability of the system
  What if we had a 1000 replicate centuries of record? How different would we perceive persistent drought risks?
  What if these 1000 replicate centuries experienced 7% reductions of streamflow due to climate change?

## Slide 13: A hidden Markov model-base stochastic streamflow generator to capture internal variability
I. Classify historical record into two states (wet and dry)
II. Fit a multivariate Gaussian dist. to the log flows in each state
III. Determine the transition probabilities between states

## Slide 14: Capturing internal variability
Historical Correlation Matrix
UC
GN
YP
WH
SW
UC
GN
YP
WH
SW
Correlation Coeff.
Preserve statistical properties of the historical record
Replicate spatial correlation between basins
Capture persistence caused by large scale climate phenomena a
Flows

## Slide 15: Stationary Envelopes (No Climate change)

## Slide 16: Capturing climate change
Perturb HMM parameters to reflect plausible changes in climate:
Scale means of dry and wet state distributions
Shift the timing of peak flows to capture changes to snowmelt
Probability Density
Annual Flow

## Slide 17: Computational experiment
Run “baseline” and “climate-adjusted” ensembles through a planning model
Each ensemble has 1,000 105 year records
Total of 210,000 years of streamflow
Notes: https://www.watereducation.org/western-water-excerpt/1922-2007-85-years-colorado-river-compact

## Slide 18: Statemod: Colorado’s water planning model
Notes: https://www.watereducation.org/western-water-excerpt/1922-2007-85-years-colorado-river-compact

## Slide 19: Statemod VS MOSART-WM scale representation illustration
Illustration for the Upper Colorado Basin where the grid represents 1/8-degree spatial resolution
Hadjimichael et al 2023 JWRPM, https://ascelibrary.org/doi/abs/10.1061/JWRMD5.WRENG-5522

## Slide 20: Statemod VS MOSART-WM scale representation illustration
Illustration for the Upper Colorado Basin where the grid represents 1/8-degree spatial resolution
Hadjimichael et al 2023 JWRPM, https://ascelibrary.org/doi/abs/10.1061/JWRMD5.WRENG-5522
v
Our HMM full natural flow modeling is at the scale of 1000+ points of diversion across the West Slope Basins (so 1000 centuries at ~1000 node locations)

## Slide 21: Deliveries to lake powell
Flow (million m3)

## Slide 22: Deliveries to lake powell
Cumulative deliveries from all basins
Flow (million m3)

## Slide 23: Deliveries to lake powell
Driest 5-year period
A
Flow (million m3)

## Slide 24: Deliveries to lake powell
Driest 10-year period
A
B
Flow (million m3)

## Slide 25: Deliveries to lake powell
A
B
A
B
Flow (million m3)
Flow (million m3)

## Slide 26: Deliveries to lake powell
A
B
A
B
Baseline HMM
Flow (million m3)
Flow (million m3)

## Slide 27: Deliveries to lake powell
A
B
A
B
Baseline HMM
Ensemble median
Flow (million m3)
Flow (million m3)

## Slide 28: Deliveries to lake powell
A
B
A
B
Baseline HMM
Ensemble 25th percentile
Flow (million m3)
Flow (million m3)

## Slide 29: Deliveries to lake powell
A
B
A
B
Baseline HMM
Ensemble 5th percentile
Flow (million m3)
Flow (million m3)

## Slide 30: Deliveries to lake powell
A
B
A
B
Baseline HMM
Flow (million m3)
Flow (million m3)
Extreme events that emerge from sampling internal variability are drier and more persistent than the observed historical record

## Slide 31: Deliveries to lake powell
A
B
A
Baseline HMM
Climate-adjusted HMM
Flow (million m3)
Flow (million m3)
B

## Slide 32: Deliveries to lake powell
A
B
A
Baseline HMM
Climate-adjusted HMM
Flow (million m3)
Flow (million m3)
B
The ‘optimistic’ climate-adjusted ensemble yields a regime change to persistently severe dry periods

## Slide 33: Changes in spatially compounding drought?
Number of drought years

## Slide 34: Changes in spatially compounding drought?
Number of drought years
Temporal definitions of drought

## Slide 35: Changes in spatially compounding drought?
Number of drought years
Spatial extent of drought

## Slide 36: Changes in spatially compounding drought?
Number of drought years
Number of years classified as drought

## Slide 37: Changes in spatially compounding drought?
Number of drought years
Baseline Median
Baseline 99th percentile
15
5
10
20
25
15
5
10
20
25
1
2
3
4
5
1
2
3
4
5

## Slide 38: Changes in spatially compounding drought?
Number of drought years
Baseline Median
Baseline 99th percentile
Climate Median
Climate 99th percentile
15
5
10
20
25
15
5
10
20
25
15
5
10
20
25
15
5
10
20
25
1
2
3
4
5
1
2
3
4
5
1
2
3
4
5
1
2
3
4
5

## Slide 39: Changes in spatially compounding drought?
Number of drought years
Baseline Median
Baseline 99th percentile
Climate Median
Climate 99th percentile
15
5
10
20
25
15
5
10
20
25
15
5
10
20
25
15
5
10
20
25
1
2
3
4
5
1
2
3
4
5
1
2
3
4
5
1
2
3
4
5
v
Even a middle-of-the-road climate change case yields substantial risk for change to long lived spatially extensive drought regimes.

## Slide 40: Theme 2 Risks & Impacts – What is needed
What are the bottlenecks for advancing regional modeling to better capture risks and impacts?
  There is a computational bottleneck in utilizing large ensemble ESM and/or regional runs at the scales needed
  It take time and effort to capture ‘holistic treatments’ of risk beyond characterizing natural hazards
  Decision relevance requires perspectives beyond ‘modelers modeling’
  There needs to be a better bridge between the physical and statistical modeling communities in better capturing extremes and risks

## Slide 41
v
Thank you! Happy to follow up in our discussion.

## Slide 42: Additional Slides

## Slide 43: Fitting the hmm
Dry state
.
Wet state
.

## Slide 44: Capturing Spatial correlation
Historical Correlation Matrix
UC
GN
YP
WH
SW
UC
GN
YP
WH
SW
Correlation Coeff.
Synthetic Correlation Matrix
UC
GN
YP
WH
SW
UC
GN
YP
WH
SW
Correlation Coeff.

## Slide 45: Identifying drought
Drought
A period when the 5-year rolling mean flow drops more than ½ standard deviation below the mean of the entire record
5