## Slide 1
Objective
Explore the effects of long-term temperature change and variability on electric capacity using an improved version of a multisector model (GCAM-USA) with details about monthly day/night load profiles.
Approach
Improve the model so it endogenously and dynamically captures the impact of future temperature change and variability on electricity load profiles.
Calculate buildings sector electricity loads in twenty-four monthly day/night segments as well as a twenty-fifth “superpeak” segment.
Dispatch capacity to meet loads in the twenty-five segments while calculating the capacity investments using superpeak demand, existing infrastructure, and power plant retirements.
Impact
Models need to consider peak loads in addition to a comprehensive multisector approach to inform long-term electric sector planning.
In a high radiative forcing climate scenario mean temperature changes will drive an approximately 5% increase in national annual electricity demands by 2100, but peak temperature changes will lead to a 15% increase in capacity and capital investments.
Impacts of long-term temperature change and variability on electricity investments
Z. Khan, G. Iyer, P. Patel, S. Kim, M. Hejazi, C. Burleyson, M. Wise, “Impacts of long-term temperature change and variability on electricity investments.” Nature Communications, 12, 1643, (2021). [DOI: 10.1038/s41467-021-21785-1]
Cumulative capital investments (2015-2100, Billion USD) under Representative Concentration Pathway (RCP) 8.5 with and without temperature impacts on electricity load profiles
Future peak temperature changes could drive increases in capital investments by 3-22% across the United States relative to a future in which temperature impacts on electricity demands are assumed to be absent.