## Slide 1
Objective
Develop and evaluate methods for predicting stress on the electric grid in a specific region based on weather data
Approach
Obtained 10 years of hourly weather and electricity load and pricing data from 16 zones in a U.S. regional transmission organization
Constructed and evaluated the ability of a penalized logistic regression model to predict grid stress events (i.e., high loads and prices) based on observed weather
Impact
Techniques explored in this paper could help improve predictions of future grid stress events in the context of evolving infrastructure configurations and environmental conditions
Understanding the conditions associated with grid stress can help inform the development of next-generation tools for representing interactions of energy and Earth systems
Evaluating Penalized Logistic Regression Models to Predict Heat-Related, Environmentally Induced Electric Grid Stress?
Bramer, L. M., Rounds, J., Burleyson, C. D., Fortin, D., Hathaway, J., Rice, J., & Kraucunas, I. (2017). Evaluating penalized logistic regression models to predict Heat-Related Electric grid stress days. Applied Energy, 205, 1408-1418 https://doi.org/10.1016/j.apenergy.2017.09.087
Researchers evaluated statistical model performance in each grid zone for individual weather variables and different combinations of variables, including lagged variables that accounted for persistent forcing. An F1 value of 1 means the model perfectly predicts grid stress. In general, maximum temperature was more predictive of grid stress for zones along the east coast compared to zones further west.
Notes: Stressed Out: Can Models Predict Grid Tolerance to Environmental Extremes?
Regression model performs well in predicting grid stress based on regional weather conditions
The Science
Understanding the environmental conditions associated with stress on the electric grid has important practical considerations, but also represents a complex scientific and modeling challenge. A research team led by scientists at Pacific Northwest National Laboratory explored how well statistical models could predict grid stress based on weather conditions in a particular region. Scientists found one type of statistical model provided predictive value and was easy to interpret.
The Impact
The electricity sector develops contingency plans so that the grid is reliable even during periods when it is stressed by extreme weather events such as heat waves. Industry planning and operations teams could use the novel statistical techniques developed through this research to better understand and predict grid stress in the context of evolving electricity infrastructure configurations and environmental conditions. The results also provide insight into the development of next-generation modeling and analysis tools to represent interactions between energy and Earth systems.
Summary
Researchers constructed statistical models based on the weather variables that tend to give rise to grid stress. They used 10 years of high time-resolution electricity load and pricing data from 16 zones in the PJM (Pennsylvania-New Jersey-Maryland) Interconnection (a regional transmission organization), along with observed weather data from the same time period. After testing several model types, researchers found that a penalized logistic regression model performed well in predicting grid stress when fit to a specific operational zone. It also revealed the weather variables most important for predicting grid stress in each zone. In addition to daily maximum temperature—typically the only variable that the electric power industry considers when making load forecasts—researchers found that other predictors of grid stress included humidity, precipitation, and lagged variables that account for persistent stresses on the grid over multiple days. In some zones, model performance was improved by including weather information from other zones, which may reflect the grid’s interconnected nature. Assuming that data are available, the methods presented in this work could be extended to other regions or used to project potential changes in grid stress associated with future climate and infrastructure scenarios.